## Slide 1: Multi Energy Systems: Investigating Hidden Flexibilities Provided by Power-to-X Considering Grid Support Strategies
MSc: Bekir Caner Yagci (4857089)
PhD: Digvijay Gusain
Supervisor: Asst. Prof. Milos Cvetkovic
Delft University of Technology
Faculty of Electrical Engineering,
Mathematics, and Computer Science

## Slide 2: Content
Introduction
    Research Problem
    Flexibility
    Research Questions
Methodology
    Multi-Energy System Design
    Energy Demand Profiles
Modelling & Analysis
    PEM Electrolyser
    Electric Heat Pump
    Power-to-X Models
    Analysis (Scenarios)
    Adjustable Power Level Controller
    Co-simulation Setup
Results

## Slide 3: Introduction - Research Problem
Variable nature of renewable energy sources introduce a great challenge for grid operator to balance the electricity supply and demand
Replacing production based on fossil fuels in industries, such as chemicals, petrochemicals, food, steel cement; leads to more sustainable and flexible multi-energy systems
Due to approximations made in model formulations (constant / linear relation between power input and energy output), flexibilities provided by P2X to network can be concealed in the simulation results
Correct efficiency characterization of P2X is crucial to understand flexibility. Inaccurate flexibility analysis of P2X may lead to increased transmission losses, higher operational cost or misinterpretation of MES capacity
In order to understand MES phenomena, complex control, flexibility or energy management analysis must be implemented and this brings a trade-off between model complexity and simulation time. Existing energy management models for MES do not consider energy cost of production (€/MWh). This results with unnecessary trading of electricity and increase in operational cost
MES: Multi Energy System
P2X: Power-to-X
DR: Demand Response

## Slide 4
” Flexibility is the ability of a component or a collection of components to response power fluctuations in power systems.”
” Hidden flexibility is the effect of modelling simplifications on flexible load (PtX) performance .”
” Optimal deployment of flexibility is the energy management strategies of flexible loads in order to make the optimal use of them in a multi-energy system.”
Introduction - Flexibility
RE: Renewable Energy
PtX: Power-to-X
An exemplary flexible load measure with the corresponding parameters [1]

## Slide 5: Introduction - Research Questions
What options exist for minimizing curtailment of renewable energy sources in MES?
  Which options are available in industrial area?
  What is the amount of excess RE (flexible capacity) in industrial area?
  Which P2X option has the best performance for the grid and the most profit for the P2X owner?
What is essential to model in order to describe the flexibility potential as precisely as possible?
  Which assumptions can be made and which physical effects should be considered?
  What should be the modelling considerations for accurate flexibility results?
What should be the energy management strategy of MES for the optimal use of resources?
  How different energy domains combined and optimized?
  How complex simulations can be created for energy management of MES?
  How to distribute excess energy between flexible loads?
MES: Multi Energy System
P2X: Power-to-X
RE: Renewable Energy
Co-simulation Approach

## Slide 6: Methodolgy – MES Design
MES: Multi Energy System
PtG: Power-to-Gas
PtH: Power-to-Heat
RES: Renewable Energy Sources
Green hydrogen (PEM Electrolyser) is one of the most convenient options as a result of hydrogen charactherisrics.
Electric heat pumps with auxiliary boilers are commonly recommended for their high efficiencies (Bode & Schmitz, 2018).
The hourly power output of RES is calculated from Renewables.ninja [2]

## Slide 7: Methodolgy – Energy Demand Profiles
 | TR [⁰C] | Tmin [⁰C] | Q0 [m3/s] | Qmax [m3/s]
Industrial P2G | 25 | 5 | 3.14E-03 | 3.85E-03
District Heating P2H | 25 | 5 | 3 | 4
The relation between ambient temperature and hydrogen & heat demand [1]
Historical ambient temperature data is used for the calculation of energy demand profiles
P2G: Power-to-Gas
P2H: Power-to-Heat
Mathematical formulation of Felten,
Baginski, and Weber (2017) model:

## Slide 8: Modelling – PEM Electrolyser
Model | Physical Domains | Modelling Approach | Dynamic Behaviour | Modelling Scale
A | Electrochemical Electrical | Analytic + Empirical | Static | Cell/Stack
B | Electrochemical Electrical Thermal | Analytic + Empirical | Static + Dynamic (ODE) | Cell/Stack + BOP
MES: Multi Energy System
ODE: Ordinary Differential Equation
BOP: Balance of Plant
Temperature dependency of electrolyser efficiency is considered
Electrolyser performance is calculated considering operational conditions (temperature, pressure)
Balance of plant elements are considered for temperature evolution

## Slide 9: Modelling – PEM Electrolyser
Thermal submodel
  BOP: circulation pump, cooling
  Static vs. First order dynamics
  Temperature, Pressure, current effects
Electrochemical:
Thermal:
Pressure:
Massflow:
BOP: Balance of Plant
Model A
Model B

## Slide 10: Modelling – Electric Heat Pump
Model | Modelling Approach | Ambient Temperature | Modelling Scale
A | Regression | Daily Average | Heat Pump
B | Regression | Hourly Measured | Heat Pump
C | Regression | Hourly Measured | Heat Pump with Auxiliary E-Boiler
Model C:
Model B & C:
Model A:

## Slide 11: Modelling – Electric Heat Pump
Table: COP results for various ambient and condenser temperatures
Figure: Theoretical Single-Stage Vapor Compression Refrigeration Cycle (C:Constant )
Pressure – Enthalpy table of refrigerant R-134a is used for enthalpy calculations with the assumptions shown in the figure

## Slide 12: Modelling – Electric Heat Pump
5th order polynomial fuction parameters for Tcondenser = 50,70 ⁰C
COP curve fitting result for Tcond = 50 ⁰C
COP curve fitting result for Tcond = 70 ⁰C

## Slide 13: Modelling - Power-to-X Models
Electrolyser & Heat Pump, calculate energy output based on power input and operating conditions
Controller, calculates Pmin, Pmax constraints for PandaPower
Storage, calculates amount of energy stored in m3
StaticGenerator, provides electrical interface and controls Qload
Power-to-Gas
Power-to-Heat

## Slide 14: Analysis
MES Analysis:
  MES analysis is carried out in order to understand the flexible capacity of MES in a specific area with selected flexible loads.
Power-to-X Model Comparison:
  Efficiency characters of different models are compared in order to investigate the effect of temperature assumptions on device performance.
Power System Analysis:
  Base case: Without any flexibility service, measuring the amount of curtailed RE with scheduled gas & heat demand profiles, None of the P2X available for flexibility service.
  First case (Hidden Flexibility): For a given flexibility request, comparing the power flow results of developed models and quantify hidden flexibility from the amount of energy output of P2X. Single P2X available for flexibility service.
  Second case (Optimal Deployment of Flexibility):With Market DR (cost signals) and Physical DR(adjustable power level control), measuring the amount of shared flexibility between P2G & P2H and quantify the reduction in total operational cost. Both P2X available for flexibility service.
MES: Multi Energy System
P2G: Power-to-Gas
P2H: Power-to-Heat

## Slide 15: Co-Simulation - Optimum Deployment of Flexibility with Hierarchical Energy Management
Objective function:
Cost function:
Constraints:
Element | Constraint | Remark
Load Static Generator External Grid |  | Operational power constraints (Device flexibility)
Transformer |  | Branch constraint (Maximum loading percentage)
Line |  | Branch constraint (Maximum loading percentage)
Bus |  | Network constraint
Element | Constraint | Remark
Load Static Generator External Grid |  | Operational power constraints (Device flexibility)
Transformer |  | Branch constraint (Maximum loading percentage)
Line |  | Branch constraint (Maximum loading percentage)
Bus |  | Network constraint

## Slide 16: Modelling – Adjustable Power Level Controller
Constraint decision:

## Slide 17: Co-Simulation - Levelized Cost of Energy
Carbon emission factors are decided depending on the pathways of Power-to-X

## Slide 18: Co-simulation Flow Chart
MES: Multi Energy System
CEMS: Community Energy Management System
OPF: Optimal Power Flow
Notes: The figure includes the
processes that allow for the storage and transport of electrical energy (Gray blocks)

## Slide 19: Simulation Tools
OpenModelica
  For fast simulation of complex dynamics from different energy domains, using object-oriented programming language
  To export FMU’s for co-simulation
Pandapower
  Optimal power flow solver
  Used for the energy management of MES for various co-simulation cases
Energysim (Co-simulation)
  Allows to implement complex simulations with reduced computational burden by using only necessary I/O’s
I/O: Input/Output
FMU: Functional Mock-up Unit
OPF: Optimal Power Flow
Co-simulation step and exchange time

## Slide 20: Results - MES Analysis

## Slide 21: Results – P2X Model Comparison

## Slide 22: Results – P2X Model Comparison

## Slide 23: References
[1] Jens Weibezahn. Data Documentation 92: Electricity, Heat, and Gas Sector Data for Modeling the Ger- man System.DIW Berlin, 2017, (ISSN 1861-1532), 2017.
[2] Stefan Pfenninger and Iain Staffell. URL http://www.renewables.ninja/.
[3] B. Felten, J. P. Baginski, and C. Weber, “KWK-Mindest- und Maximaleinspeisung - Die Erzeu- gung von Zeitreihen für die Energiesystemmodellierung,” no. 10, 2017.
[4] A. Bloess, W. P. Schill, and A. Zerrahn, “Power-to-heat for renewable energy integration: A review of technologies, modeling approaches, and flexibility potentials,” Appl. Energy, vol. 212, no. August 2017, pp. 1611–1626, 2018.
[5] J. Webster and C. Bode, “Implementation of a Non-Discretized Multiphysics PEM Electrolyzer Model in Modelica,” Proc. 13th Int. Model. Conf. Regensburg, Ger. March 4–6, 2019, vol. 157, pp. 833–840, 2019.

## Slide 24: Multi Energy Systems: Investigating Hidden Flexibilities Provided by Power-to-X Considering Grid Support Strategies
MSc: Bekir Caner Yagci (4857089)
PhD: Digvijay Gusain
Supervisor: Asst. Prof. Milos Cvetkovic
E-mail: B.C.Yagci@student.tudelft.nl
Version Control: https://github.com/caneryagci/Multi-Energy-Systems-Thesis-Project.git